## Slide 1: CSCI3420 Tutorial 6
Week 7
K.K. Tong
Single Cycle CPU: A Case Study
Project Phase 2

## Slide 2: Overview
CPU can be abstracted as state machine
An execution that
  Read contents from state element
  Send values through combinational logic
  Write contents to state element
State Element
#1
Combinational Logic
State Element
#2

## Slide 3: Overview
A single clock CPU
State Element
Combinational Logic
PC
Address
Instruction
Memory
Instruction
Register #
Data
Register #
Register #
Register
ALU
A
D
ddress
ata
Data
Memory

## Slide 4: Basic dataflow
Essential components: instruction fetch unit, branch unit, registers, ALUs, memory, control unit
Instruction fetch unit
Branch unit
Registers
ALUs
Memory
Control unit

## Slide 5: Flow of execution
Read Inst
Decode Inst, pass to control
Control sends signals
Registers read
Use ALU/Jump
Memory read
Update PC
Write registers

## Slide 6: Single-Cycle CPU - A Case Study
Only focus on a subset of MIPS
  arithmetic / logic: add, sub, and, or
  memory-referenced: lw, sw
  branch: beq
A Case Study
  It covers the main concept

## Slide 7: Datapath components
Multiplexer (data selector)
Instruction fetch unit
Register file
ALU
Sign-extension unit (16 bit -> 32 bit)
Memory (instruction / data)

## Slide 8: Multiplexer
0
1
Mux
Mux
0
1
2
3
sel
sel

## Slide 9: Instruction fetch unit
Fetching instructions and increasing the program counter by 4
PC
Read
Address
Instruction
Memory
Instruction
ADD
4

## Slide 10: Instruction fetch unit
Execute
  0x4000 addi $s0, $zero, 5
  0x4004 and $s0, $s0, $zero
  0x4008 addi $s0, $s0, 1
PC
Read
Address
Instruction
Memory
Instruction
ADD
4
PC update when the clock rise
addi $s0, $zero, 5
0x4000
0x4004

## Slide 11: Instruction fetch unit
Execute
  0x4000 addi $s0, $zero, 5
  0x4004 and $s0, $s0, $zero
  0x4008 addi $s0, $s0, 1
PC
Read
Address
Instruction
Memory
Instruction
ADD
4
PC update when the clock rise
and $s0, $s0, $zero
0x4004
0x4008

## Slide 12: Register File (Read)

## Slide 13: Register File (Write)

## Slide 14: ALU
ALU Operation | Desired ALU action
000 | and
001 | or
010 | add
110 | sub
Zero
ALU
ALU
result
ALU Operation
3
Obtained from the specification of the ALU
OP | MIPS Instruction
add | lw, sw,…
sub | beq,…

## Slide 15: Data memory & sign extension
MemWrite
Address
Write
data
Data
Memory
Read
data
MemRead
Sign
extend
16
32
shift
left 2
Byte address
Word address
Why need sign extend?
beq $s1, $s2, 25 => if($s1 == $s2) go to PC+4+100
Address | Instruction
100 | add $t1, $t1, $s6
104 | sub $t1, $t1, $s6
108 | addi $s1, $s1, 1
1 word = 4 bytes (in 32-bit Architecture)
32-bit ALU !

## Slide 16: MIPS instruction type
R-type
I-type
J-type
op | rs | rt | rd | shamt | funct
op | target address
op | rs | rt | immediate
31:26 25:21 20:16 15:11 10:6 5:0
31:26 25:21 20:16 15:0
31:26 25:0
Read register 1&2: [25:21], [20:16]
Register destination: [15:11] (R-type) or [20:16] (I-type)
Base register for calculating address: [25:21]
Offset for beq/load/store: [15:0]
0
35 /43
16
lw,sw,beq,…
j,…
add,sub,…
Field | Description
o | Instruction opcode
s | First source register
t | Second source register
d | Destination register
a | Shift amount
f | Function

## Slide 17: Simple datapath for this example
Given the below components, how to connect them to form a single cycle CPU?
PC
Read
Address
Instruction
Memory
Instruction
ADD
4
RegWrite
Registers
Read
data 1
Read
data 2
Read
register 1
Read
register 2
Write
register
Write
data
5
5
5
32
32
32
Zero
ALU
ALU
result
ALU Operation
3
MemWrite
Address
Write
data
Data
Memory
Read
data
MemRead
Sign
extend
16
32
shift
left 2
offset

## Slide 18: Simple datapath for this example
MemToReg
MemRead
MemWrite
R
e
a
d
a
d
d
r
e
s
s
I
n
s
t
r
u
c
t
i
o
n
[
3
1
–
0
]
Add
4
1
6
3
2
Zero
M
u
x
M
u
x
M
u
x
Shift
left 2
ALU
ALU
result
Add
ALU
result
Address
Write
data
Data
Memory
Read
data
ALUSrc
RegWrite
PCSrc
Instruction
memory
Registers
Sign
extend
PC
Read
data 1
Read
data 2
Read
register 1
Read
register 2
Write
register
Write
data
3 ALU Operation
M
U
x
Register destination: [15:11] (R-type) or [20:16] (I-type)

## Slide 19: Basic Datapath
add $s1, $s2, $s3
MemToReg
MemRead
MemWrite
R
e
a
d
a
d
d
r
e
s
s
I
n
s
t
r
u
c
t
i
o
n
[
3
1
–
0
]
Add
4
1
6
3
2
0
Zero
M
u
x
1
1
M
u
x
0
1
M
u
x
0
Shift
left 2
ALU
ALU
result
Add
ALU
result
Address
Write
data
Data
Memory
Read
data
ALUOp[2-0]
ALU
control
ALUSrc
RegWrite
RegDst
PCSrc
Instruction
memory
Registers
Sign
extend
PC
Read
data 1
Read
data 2
Read
register 1
Read
register 2
Write
register
Write
data
Instruction [25-21]
Instruction [20-16]
Instruction [15-11]
Instruction [15-0]
Instruction [5-0]
$s2
$s3
$s1
($s2)
($s3)
($s2)+($s3)
op | rs | rt | rd | shamt | funct
31:26 25:21 20:16 15:11 10:6 5:0
R-type:
1
M
u
x
0
PCSrc
Branch

## Slide 20: Basic Datapath
lw $s0, (100)$s1
MemToReg
MemRead
MemWrite
R
e
a
d
a
d
d
r
e
s
s
I
n
s
t
r
u
c
t
i
o
n
[
3
1
–
0
]
Add
4
1
6
3
2
0
Zero
M
u
x
1
1
M
u
x
0
1
M
u
x
0
Shift
left 2
ALU
ALU
result
Add
ALU
result
Address
Write
data
Data
Memory
Read
data
ALUOp[2-0]
ALU
control
ALUSrc
RegWrite
RegDst
PCSrc
Instruction
memory
Registers
Sign
extend
PC
Read
data 1
Read
data 2
Read
register 1
Read
register 2
Write
register
Write
data
Instruction [25-21]
Instruction [20-16]
Instruction [15-11]
Instruction [15-0]
Instruction [5-0]
$s1
$s0
100
($s1)
Mem[($s1)+100]
100
op | rs | rt | immediate
31:26 25:21 20:16 15:0
I-type:
1
M
u
x
0
Branch

## Slide 21: Basic Datapath
beq $s0, $s1, 2500
MemToReg
MemRead
MemWrite
R
e
a
d
a
d
d
r
e
s
s
I
n
s
t
r
u
c
t
i
o
n
[
3
1
–
0
]
Add
4
1
6
3
2
0
Zero
M
u
x
1
1
M
u
x
0
1
M
u
x
0
Shift
left 2
ALU
ALU
result
Add
ALU
result
Address
Write
data
Data
Memory
Read
data
ALUOp[2-0]
ALU
control
ALUSrc
RegWrite
RegDst
PCSrc
Instruction
memory
Registers
Sign
extend
PC
Read
data 1
Read
data 2
Read
register 1
Read
register 2
Write
register
Write
data
Instruction [25-21]
Instruction [20-16]
Instruction [15-11]
Instruction [15-0]
Instruction [5-0]
$s0
$s1
($s0)
($s1)
Branch
op | rs | rt | immediate
31:26 25:21 20:16 15:0
I-type:
1
M
u
x
0

## Slide 22: Control Unit
MemRead
MemWrite
R
e
a
d
a
d
d
r
e
s
s
I
n
s
t
r
u
c
t
i
o
n
[
3
1
–
0
]
Add
4
1
6
3
2
0
Zero
M
u
x
1
1
M
u
x
0
1
M
u
x
0
Shift
left 2
ALU
ALU
result
Add
ALU
result
Address
Write
data
Data
Memory
Read
data
ALUOp[2-0]
ALU
control
ALUSrc
RegWrite
RegDst
PCSrc
Instruction
memory
Registers
Sign
extend
PC
Read
data 1
Read
data 2
Read
register 1
Read
register 2
Write
register
Write
data
Instruction [25-21]
Instruction [20-16]
Instruction [15-11]
Instruction [15-0]
Instruction [5-0]
Branch
1
M
u
x
0
MemToReg
Control Signal

## Slide 23: Control Unit
R
e
a
d
a
d
d
r
e
s
s
I
n
s
t
r
u
c
t
i
o
n
[
3
1
–
0
]
Instruction
memory
PC
Main
Control
Instruction [31-26]
ALU
Control
Instruction [5-0]
RegDst
Branch
MemRead
MemtoReg
ALUOp
MemWrite
ALUSrc
RegWrite
ALU

## Slide 24: Complete Datapath with Control Unit

## Slide 25: Control unit
Instruction | RegDst | ALUSrc | MemtoReg | RegWrite | MemRead | MemWrite | Branch | ALUOp1 | ALUOp0
R-format | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
lw | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
sw | X | 1 | X | 0 | 0 | 1 | 0 | 0 | 0
beq | X | 0 | X | 0 | 0 | 0 | 1 | 0 | 1

## Slide 26
Signal | Effect when setting as 0 | Effect when setting as 1
RegDst | The register destination number for the write register comes from the rt field (bits 20:16) | The register destination number for the write register comes from the rd field (bits 15:11)
RegWrite | None | The register on the Write register input is written with the value on the write data input.
ALUSrc | The second ALU operand comes from the second register file output (Read Data 2) | The second ALU operand comes from the sign-extended, lower 16 bits of instruction
PCSrc | The PC is replaced by the output of the adder that computes the value of PC + 4 | The PC is replaced by the output of the adder that computes the branch target
MemRead | None | Data memory contents designed by the address input are put on the Read data output
MemWrite | None | Data memory contents designed by the address input are replaced by the write data input
MemtoReg | The value fed to the register write data input comes from the ALU | The value fed to the register Write data input comes from the data memory

## Slide 27: Control unit
ALU Control – Mapping of the input and output
  Input: ALUOp (2-bit) + funct (6-bit, instruction [5:0])
  Output: 3-bit ALU Operation

## Slide 28: Project Phase 2
Specification
Materials
Submission
Test cases

## Slide 29: Project Phase 2
In order to have a more in depth understanding of CPU architecture, you have to write assembly programs, a single-cycle simulator and a multi-cycle pipelined simulator of a simplified CPU.
In phase 2, you have to write a single cycle simulator in standard C, so that you gain experience in understanding the datapath design and how instructions execute in single cycle machine.

## Slide 30: Project Phase 2

## Slide 31: Project Phase 2
Architecture in phase 2:
  Each machine word has 32 bits.
  Memory size is exactly 64Kb (16 bits are sufficient to specify an address).
  All store and load operations are word-aligned.
  Every instruction takes one machine word.
  The machine is big-endian, i.e. the most significant byte comes first.
  The registers available are listed in table 1.
  You are required to implement only a reduced subset of some usual CPU instructions, as shown in table 2.
  The encoding of the instructions is given in table 3. For the representation, the row shows what is contained in a field, and the header row shows the number of bits of each field.
Register Name | Remarks | Remarks
$zero | Always has value 0 | 0x00
$ra | Return address | 0x01
$fp | Frame pointer | 0x02
$sp | Stack pointer | 0x03
$hi | High-word | 0x04
$lo | Low-word | 0x05
$s1, $s2,...,$s26 | General purpose registers | 0x06,0x07,...

## Slide 32: Project Phase 2
Instruction Set
Instruction | Usage | Binary Representation |  |  |  |  | 
 |  | 6 | 5 | 5 | 5 | 5 | 6
Add | add rd,rs,rt | 0x0f | rs | rt | rd | 0 | 0x11
Add Immediate | addi rt,rs,imm | 1 | rs | rt | imm |  | 
Subtract | sub rd,rs,rt | 0x0f | rs | rt | rd | 0 | 0x12
Multiplication | mult rs,rt | 0x0f | rs | rt | 0 |  | 0x18
Division | div rs,rt | 0x0f | rs | rt | 0 |  | 0x1a
And | and rd,rs,rt | 0x0f | rs | rt | rd | 0 | 0x2a
Or | or rd,rs,rt | 0x0f | rs | rt | rd | 0 | 0x2b
Shift Left Logical Variable | sllv rd,rt,rs | 0x0f | rs | rt | rd | 0 | 1
Shift Right Logical Variable | srlv rd,rt,rs | 0x0f | rs | rt | rd | 0 | 2
Load word | lw rt,offset (rs) | 0x1a | rs | rt | offset |  | 
Store word | sw rt,offset (rs) | 0x1b | rs | rt | offset |  | 
Set Less Than | slt rd,rs,rt | 0x0f | rs | rt | rd | 0 | 0x25
Branch on Not Equal | bne rs,rt,label | 2 | rs | rt | offset |  | 
Jump | j target | 3 | target |  |  |  | 
Jump Register | jr rs | 0x0f | rs | 0 |  |  | 3
Jump And Link | jal target | 4 | target |  |  |  | 

## Slide 33: Project Phase 2
Simulator
  The input to the simulator is a binary file, where every 4 bytes represent a word in big-endian format.
  You may assume that the input file size is always a multiple of 4.
  Your simulator should treat each word in the input as an instruction and try to simulate it.
  Your simulator should halt when the fetched instruction is 0x0.
  Your simulator should also halt when the fetched instruction is invalid (which means instructions not shown in Table 3). In this case, you need to store your student ID in register $s26.
  For simplicity, all rs and rt for mult and div should only contain non-negative numbers.

## Slide 34: Project Phase 2
Task: Implement 22 functions
  “run_program_counter()” is completed for you as an example
  void run_program_counter(unsigned Next, unsigned *PC) {
  *PC = Next;
  }

## Slide 35: Project Phase 2

## Slide 36: Project Phase 2
Provided Materials
  simulator_linux
    reference simulator compiled in linux1 of our department
  complie.sh
    shell script to compile and run your simulator
  asm_linux
    assembler program compiled in linux1 of our department
  *.asm, *.asc
    sample code for your testing
  bz162.zip
    a binary editor for you to add invalid instructions
  components.h
    header file defines the data structure representing each component
  simulator.c
    main function of the simulator
  phase2.h
    header file defines the functions you have to complete
  phase2.c
    Program skeleton (your code here)

## Slide 37: Project Phase 2
Testing your program
  Compare with sample simulator:
  “./simulator_linux machine_code.asc”
  Generate *.asc from MIPS:
  “./asm_linux assembly_code.asm machine_code.asc”
  Generate invalid instructions:
  Use BZ!
  P.S. simulator_linux and asm_linux can be run in Linux only.

## Slide 38: Project Phase 2
How to create invalid instructions?
  Unzip bz162.zip
  Open the Bz.exe
  In Bz.exe, click “File->Open” to open *.asc file.
  Then you will see the content of that file.
  You can change the content to a invalid machine code in this editor

## Slide 39: Project Phase 2
Submission:
  Submit only “phase2.c”.
  You MUST submit the C file to the submission system on our course homepage (within CUHK network), otherwise, we will NOT mark your assignment. The details of how to use the system will be announced later.
  Please limit the file size to be less than 1MB.
  Plagiarism will be seriously punished.
  Late submission will NOT be accepted, and the submission time will be determined according to our submission system.

## Slide 40: Project Phase 2
Test cases:
  mult
  div
  add_sub
  addi
  addi_neg
  and_or
  sllv_srlv
  lw
  sw
  slt
  slt_neg
  bne
  j
  jr
  jal
  zero_register
  Invalid instruction