## Slide 1: Constraint-Based Dynamic Energy Management in Energy Harvesting Embedded System WeiYing Yi 1155026053 Department of Computer Science and Engineering Faculty of Engineering The Chinese University of Hong Kong

## Slide 2: Core Idea
Reference Paper
  S. O´ . Murphy, O´ . Manzano, and K. Brown, “Design and evaluation of a constraint-based energy saving and scheduling recommender system,” in Principles and Practice of Constraint Programming, ser. Lecture Notes in Computer Science, G. Pesant, Ed. Springer International Publishing, 2015, vol. 9255, pp. 687–703. [Online]. Available: http://dx.doi.org/10.1007/978-3-319-23219-5 47
Saving energy while keeping good enough performance of the system (home appliances)
Adapted the idea into embedded systems powered by renewable energy
Example: wireless sensing node with small solar cell and small battery
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 3: Assumption
Convert continuous time t to discrete intervals T
  10 mins per interval, 144 intervals per day
Solar energy prediction function F(T) with 100% accuracy
Sensor node consists of 7 sensors and 1 radio link
Experiment data are self-define
Definition:
  Wasted Energy: not used by any of the 8 devices
  Endurance: # of intervals with non-zero energy consumption
  Data quality: evenly distribute the sampling tasks
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 4: Issues
Nature of solar energy => Unstable
  Not power line as the reference paper
Battery capacity => Limited
  Small battery for embedded system
Charging efficiency => < 100%
  Usually 80%
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 5: Issues: Unstable Solar Energy
Solar energy => Battery => Static DC power(averaging interval energy consumption)
Maximal system endurance
Require large enough battery capacity
Approach | Wasted Energy | Endurance/144
1 | 70.83 | 144
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 6: Issues: Limited Battery Capacity
Solar energy => Battery => Static DC power (averaging interval energy consumption)
Energy wasted when battery is full
Approach | Wasted Energy | Endurance/144
1 | 70.83 | 144
2 | 216.42 | 73
3 |  | 
4 |  | 
5 |  | 
6 |  | 
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 7: Issues: Charging Efficiency < 100%
Solar energy => Sensor node
No battery => No energy wasted for charging
Energy consumption of sensor node adapts to solar energy
Approach | Wasted Energy | Endurance/144
1 | 70.83 | 144
2 | 216.42 | 73
3 | 19.6 | 55
4 |  | 
5 |  | 
6 |  | 
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 8: Issues: Endurance Too Low
Solar energy => Battery => Sensor node
Energy consumption of sensor node adapts to solar energy
Energy wasted as charging efficiency < 100%
Approach | Wasted Energy | Endurance/144
1 | 70.83 | 144
2 | 216.42 | 73
3 | 19.6 | 55
4 | 70.69 | 59
5 |  | 
6 |  | 
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 9: More Improvement?
We want less wasted energy
We want larger endurance
Why you are so greedy?
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 10: More Improvement?
We want less wasted energy
  Reduce the solar energy stored into battery
  Energy consumption of the sensor node adapts to the solar energy
We want larger endurance
  Take the future into account
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 11: More Improvement?
Proposed system
Hardware
  Sensor node can access the
  harvest energy directly
  Or access energy stored in energy
Software
  Application Rate Layer
  Real-time Scheduling Layer
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 12: More Improvement?
Application Rate Layer
  COP
  Objective: Find the optimal operational rate for each interval of each devices of the sensor node, such that the wasted energy is minimized while have good enough endurance
  Assign each type of data a reward value, i.e. reward_CO = 10, reward_RH = 5
  Achieved by maximized the total rewards of the next K intervals while satisfying energy constraint
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 13: More Improvement?
Application Rate Layer with K = 3
Significant improvement in wasted energy
Improvement in endurance
Approach | Wasted Energy | Endurance/144
1 | 70.83 | 144
2 | 216.42 | 73
3 | 19.6 | 55
4 | 70.69 | 59
5 | 4.09 | 61
6 |  | 
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 14: More Improvement?
Application Rate Layer with K = 6
Improvement in endurance at the expense of slight incensement of wasted energy
Approach | Wasted Energy | Endurance/144
1 | 70.83 | 144
2 | 216.42 | 73
3 | 19.6 | 55
4 | 70.69 | 59
5 | 4.09 | 61
6 | 4.41 | 62
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 15: More Improvement?
Real-time Scheduling Layer
  Input is from the Application Rate Layer
  i.e. optimal operation rate {6, 6, 6, 6, 5, 1, 1, 2} in 10 minutes interval
  Divided the 10 minutes interval into 10 smaller intervals, each small interval is 1 minute
  Objective: We want to have good data quality of each type of sensors.
  Achieved by evenly distributed the samples in the 10 one minute intervals
    CO: {1, 1, 0, 1, 0, 1, 0, 1, 0, 1}
    SO2: {1, 1, 0, 1, 0, 1, 0, 1, 0, 1}
    O3: {1, 1, 0, 1, 0, 1, 0, 1, 0, 1}
    NO2: {1, 1, 0, 1, 0, 1, 0, 1, 0, 1}
    PM: {1, 1, 0, 1, 0, 1, 0, 1, 0, 1}
    TEMP: {0, 1, 0, 1, 0, 1, 0, 1, 0, 1}
    RH: {0, 0, 1, 0, 0, 0, 0, 0, 0, 0}
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■

## Slide 16: Conclusions
Our approach is able to:
  Fully utilized the harvested energy
  Improvement in reduce the amount of wasted energy
  Improvement in increase the endurance
  Sufficient good data quality with given operational rates of all devices
Core Idea Assumptions Issues More Improvements? Conclusions
■ ■ ■ ■ ■

## Slide 17: Thank you!